## Slide 1: Python Development Schemes for Monte Carlo Neutronics on High Performance Computing
Jackson P. Morgan & Kyle E. Niemeyer
The Center for Exascale Monte Carlo Neutron Transport (CEMeNT)
Oregon State University
SciPy 2022
Austin, TX
July 17th, 2022
  This work was supported by the Center for Exascale Monte-Carlo Neutron Transport (CEMeNT) a PSAAP-III project funded by the Department of Energy, grant number: DE-NA003967

## Slide 2: Introduction

## Slide 3: Neutron Transport
Trying to answer when how and when neutrons interact with a domain
Applications:
  Cancer radio therapy development
  Power reactor
  Other governmental implementations

## Slide 4: Neutron Transport and HPC
ENIAC – 1946
First general programable computer circa 1946
There at the beginning…
There now
El Capitan – 2023
Heterogeneous exa-scale machine

## Slide 5: Monte Carlo Methods
Can we use statistics and event rates to model a system?
Traditional numerical methods (deterministic methods) get an exact solution to an estimated problem
Monte Carlo gives an estimated solution to an exact problem

## Slide 6: Monte Carlo Neutronics
Σscat = ½ [cm-1]
Σcap = ½ [cm-1]
Σtotal = 1 [cm-1]
Are we safe?

## Slide 7: Monte Carlo Neutronics
Material Data (statistical likelihoods)
Equations where can relate a distance to a probability
List of events that could possible happen (scatter, absorption, transmission)
ξ: random number [0,1]
Σt: total cross section

## Slide 8: Monte Carlo Neutronics: Round 1
n
Σscat = ½ [cm-1]
Σcap = ½ [cm-1]
Σtotal = 1 [cm-1]
Events:
Roll a random number = 0.345
Compute distance to event S = 1.06 cm
Move the particle
Roll a new random number = 0.544
Determine new event type > 0.5
Tally Absorption

## Slide 9: Monte Carlo Neutronics Round 2
n
Σscat = ½ [cm-1]
Σcap = ½ [cm-1]
Σtotal = 1 [cm-1]
Events:
Roll a new random number = 0.342
Determine new event type < 0.5
Reroll
Move
Tally event

## Slide 10: Monte Carlo is Dirt Slow!
To get a decent solution we will need to do this over
and over…
and over…
…
and over…
and over…
and over…
and over…
…

## Slide 11: Adding Complexity
Other events we can add
  Scattering
  Fissions
Other physics we can capture
  Delayed neutron production
  Change of material
  Change of time step
  Variance reduction mechanisms

## Slide 12: MC/DC

## Slide 13: MC/DC: Monte Carlo / Dynamic Code
Kobyashi Problem: Image courtesy Ilham Variansyah
Dynamic neutron transport solver made for rapid methods exploration at high performance computing and exa-scale
Target various hardware architectures
Written in Python

## Slide 14: MC/DC–TNT: Toy Neutronics Testbed
Mono-energetic, slab-geometry, transient tallies, fission, event-based, with surface tracking
Architecture targets: Nvidia GPUs and x86 CPUs
Validated with analytic solutions [1]
Vacuum
Vacuum
  L = 40cm, ν = 2.3, Δx = 0.49cm Σcap = Σscat = Σfis = 1/3cm-1

## Slide 15: MC/DC–TNT
Modularity in mind
10 accelerated functions
Advance implemented on hardware target
User aware kernel production (nothing off the shelf)
.
└── mcdc_tnt
├── numba_kernels
│ ├── cpu
| ├── pyopenmp
│ └── cuda
├── pk_kernels
├── hcgl_kernels
└── pure_py_kernels

## Slide 16: Event-Based MC Transport Flow Chart
Advance till collision (tallying in appropriate bins)
Still in space and time?
Sample event
Event Type
Scatter
Add fissions
Capture
Cleanup
Population control

## Slide 17: Methods of Acceleration

## Slide 18: Heterogeneous Targeting: Python Glue
Python serves as glue code
Native Python modules used produce and just-in-time (JIT) schemes
Can target multiple architecture types

## Slide 19: PyKokkos
Python library that implements parts of Kokkos Portability framework [2]
Brand new and under active development
Currently building out HIP functionality

## Slide 20: Numba + CUDA
Converts Python code then implements the LLVM compiler [3]
Industry support and active development
Often operates on pure Python code
Experimental full implementation of OpenMP [4]

## Slide 21: HCGL and Mako Templating Engine
Implemented on PyFR [5] at petascale [6]
Code-generating libraries to compile templated code
Our implementation plugs into PyCUDA and g++

## Slide 22: Results

## Slide 23: Runtime Test Problem
Sub-critical slab with initial population of 1×108 particles
Validated with MC/DC
Follow particles till death
Vacuum
Vacuum
  L = 1cm, ν = 2, Δx = 0.01cm Σcap = Σscat = Σfis = 1/3cm-1

## Slide 24: Performance: CPU
Method of Implementation | Compile Time [s] | Run Time [s]
Pure Python* | N/A | 52970
Numba (Native threading) | 5.28 | 232.3
Numba PyOmp | 5.66 | 382.3
PyKokkos | 37.50 | 158.4
Integration test problem: L = 1cm, Δx = 0.01cm, Σf = Σc = Σs = 1/3 cm-1, ν = 2, vacuum boundary conditions on LHS and RHS w/ 1 × 108 Initial particles
16 threads on an i7-10875H CPU
*one thread

## Slide 25: Performance: GPU Implementation
Method of Implementation | Compile Time [s] | Run Time [s]
Numba | 6.25 | 179.36
PyKokkos | 39.72 | 385.24
HCGL (PyCUDA) | 2.45 | 160.53
1 single GPU (NVIDIA TeslaV100 at 1530MHz w/ 16GB) on 1 Lassen node
Integration test problem: L = 1cm, Δx = 0.01cm, Σf = Σc = Σs = 1/3 cm-1, ν = 2, vacuum boundary conditions on LHS and RHS w/ 1 × 108 Initial particles

## Slide 26: Conclusions and Future Work

## Slide 27: Difficulty of Implementation
Numba is simple
Pykokkos is more difficult
HCGL is very difficult but more performant

## Slide 28: Performance
Ease of use inversely proportional to max performance
Every method is very performant! (relative to non-accelerated Python)
Diminishing returns for more difficult implementations

## Slide 29: Future Work
Complete transient tally implementation for all methods
Test deployment on new hardware
Implement testbed in C++
Implement Numba on MC/DC to accelerate pure Python code and gain fine grain parallelism

## Slide 30: Acknowledgments
Special thanks to:
  Ilham Variansyah
  Aaron Reynolds
  CEMeNT Team and Associated Folks!

## Slide 31: Citations
[neu] https://ieeexplore.ieee.org/document/6880250
[1] Ganapol B.D., Baker, R. S., Dahl, J. A., & Alcouffe, R. E. (2001). Homogeneous Infinite Media Time-Dependent Analytical Benchmarks. International Meeting on Mathematical Methods for Nuclear Applications, 836(December), 1–4.
[2] Awar, N. Al, Zhu, S., Biros, G., & Gligoric, M. (2021). A performance portability framework for python. Proceedings of the International Conference on Supercomputing, 467–478. https://doi.org/10.1145/3447818.3460376
[3] Lam, S. K., Pitrou, A., & Seibert, S. (2015). Numba: A LLVM-Based Python JIT Compiler. Proceedings of the Second Workshop on the LLVM Compiler Infrastructure in HPC. https://doi.org/10.1145/2833157.2833162
[4] T. G. Mattson, T. A. Anderson, G. Georgakoudis, K. Hinsen, and A. Dubey, “PyOMP: Multithreaded Parallel Programming in Python,” Comput. Sci. Eng., vol. 23, no. 6, pp. 77–80, Nov. 2021, doi: 10.1109/MCSE.2021.3128806.
[5] Witherden, F. D., Farrington, A. M., & Vincent, P. E. (2014). PyFR: An open source framework for solving advection-diffusion type problems on streaming architectures using the flux reconstruction approach. Computer Physics Communications, 185(11), 3028–3040. https://doi.org/10.1016/j.cpc.2014.07.011
[6] Witherden, F. (2021). Python at petascale with PyFR or: how I learned to stop worrying and love the snake. Computing in Science & Engineering, 9615(c), 1–1. https://doi.org/10.1109/mcse.2021.3080126

## Slide 32: Backmatter Slides

## Slide 33: Code Sample
Vectorized Multiplication in Each Method

## Slide 34: Other Acceleration Techniques in Python
Cython (able to use C++ standard parallelism)
PyCUDA and PyOpenCL (used but not directly)
MPI4Py (Does not accelerate code, only runs more of it)
Python CUDA
Pure Numba / SciPy implementations (C under the hood)
Build your own!

## Slide 35: Planed Explorations within MC/DC
Fully transient Monte Carlo
Intrusive UQ
Dynamic Quasi Monte Carlo
Dynamic Weight Windows
Population Control Methods
Python Based Parallelization
Asynchronous GPU scheduling
Machine Learning MPI scheduling

## Slide 36: Future Development Path of MC/DC
Address Numba issues in MC/DC
  Replace JITClass with Numba structured array
  Runtime and memory profiling
Write event-based MC/DC (pure Python + MPI4Py)
  Reuse and exploit existing MC/DC (history-based) modules with Python decorator
Integrate findings from MC/DC-TNT
  PyKokkos, Numba, PyOMP, Mako templating

## Slide 37: AVURV Benchmark Descirption
We can simulate fission by having c>1
NTE with initial source

## Slide 38: Science Python & HPC: Bigger Picture
Enables rapid methods development for complex systems [7]
Off the shelf codes for science applications available [8]
There is a trade off in performance in benchmarks [9]
A rich environment or high productivity in science [10]
Allows nuclear folks to better interface with other fields!
Can alleviate the need for C++ testbeds as initial performance analysis of methods can be examined
[7] Barba, L. A., Klockner, A., Ramachandran, P., & Thomas, R. (2021). Scientific Computing With Python on High-Performance Heterogeneous Systems. Computing in Science & Engineering. https://doi.org/10.1109/MCSE.2021.3088549
[8] Bogdan Opanchuk, Daniel Ringwalt, Lev E. Givon, & SyamGadde. (2021). Reikna(0.7.4). http://reikna.publicfields.net/en/latest/
[9] Oden, L. (2020). Lessons learned from comparing C-CUDA and Python-Numbafor GPU-Computing. Proceedings -2020 28th Euromicro International Conference on Parallel, Distributed and Network-Based Processing, PDP 2020, 216–223. https://doi.org/10.1109/PDP50117.2020.00041
[10] L. A. Barba, "The Python/Jupyter Ecosystem: Today’s Problem-Solving Environment for Computational Science," in Computing in Science & Engineering, vol. 23, no. 3, pp. 5-9, 1 May-June 2021, doi: 10.1109/MCSE.2021.3074693.